## Slide 1
UBSUP - DTF project - KENYA Operation of a Co-composting facility

## Slide 3
Keywords User’s guide page 4

## Slide 4: Co-composting shed User’s guide page 4
3 Areas of 2 chambers each:
Area 1: offload and storage of raw material (waste and UDDT waste) and storage of mature compost
Area 2 and 3: co-composting process. 2 windrows maximum

## Slide 5: Co-composting shed in Oloolaiser

## Slide 6: Co-composting shed in Benin (West Africa)

## Slide 7
Material for co-composting User’s guide page 5 and 6
YES
NO

## Slide 8
Composition of a windrow User’s guide page 7 and 8
N = Nitrogen
C = Carbon
Nitrogen and Carbon is food for micro-organisms

## Slide 9
Green waste Co-composting project in Benin

## Slide 10
Brown waste Co-composting project in Benin

## Slide 11
Composition of a windrow User’s guide page 7 and 8
Consecutive layers:
UDDT matter and screening residue (2 cm)
Brown waste (10 cm)
Green waste (5 cm)
Dimension:
Length: 3m ; Width: 2.5m ; Height: 1.6m
Ideal combination to be determined by YOU (trials and errors)
Too wet: add more brown waste
Too dry: add more green waste

## Slide 12
Windrow layers Co-composting project in Benin

## Slide 13
Windrow turning User’s guide page 9 and 10
Co-composting process: 3 months
Turning  Air supply
Favour growth of micro-organism
Prevent odours
Turning schedule to be determined by YOU (trial and errors)
Recommendation: 3 to 6 turnings in total

## Slide 14
Windrow turning Co-composting project in Benin

## Slide 15
Evolution of a windrow: moisture and temperature User’s guide page 11 and 13
Moisture content between 40 to 60% all throughout
Temperature must not exceed 70°C because it prevents microbiological activities.
Week 0 to 1: around 65°C  favour rapid composting and kill weed seeds, insect larvae and pathogens
Week 1 to 7: gradual decrease from 65°C to ambient temperature
Week 7 to 12: stabilization at ambient temperature

## Slide 16
Maturation process User’s guide page 14
Last turning: day 50th
Colour  Dark brown (soil like)
Temperature  below 50°C
Small insects and fungus (white stains) necessary to break down complex organic material

## Slide 17
Mature compost Co-composting project in Benin

## Slide 18
Screening / storage and bagging User’s guide page 15
Mature compost is screened onto the sieve (5 to 10mm mesh size)
Fine compost is stored in bulks or bags before selling.
Compost cannot be stored in bags more than 1 year (risk of dry-out)
Screening residue used to make a new windrow

## Slide 19
Screening Co-composting project in Benin

## Slide 20
Bagging Co-composting project in Benin